FINAL PROJECT
German Ilyin

KBTU 2011
# System Overview

## General View
Here is the general view of my system.

It consists of 6 host blocks, 7 router blocks, 6 red link blocks, 4 blue link blocks and 5 green link blocks.
## Host
### Host General View
The main parts of one host block are 3 Random Integer Blocks, Event Based Random Number, Time Based Entity generator, Set Attribute block. Other blocks are not required but necessary for observation and etc.
### Host Entity generation
For Entity generation we use Event-Based Random Number(EBRN) block. It's set to use Poisson distribution.
Time based Entity generator is connected to EBRN on port t. So the generation of each next entity depends on Poisson distribution of EBRN.

### Host Entity Attributes generation
Each packet initially consists of such attributes: type – packet type (0 – UDP, 1- TCP), size - packet size (0 – 256/512, 1 – 512/1024), dest – packet destination (host 1-6 respectively), from – packet source (host 1-6 respectively)

For attributes generation we use Random Integer blocks. Each of them is used for Packet type generation, Packet size generation, Packet destination generation. This block uses uniform distribution.

For destination generation “M-ary number” parameter is 6, so values between 0 and 5 will be generated.
## Links
Link block looks like this

It consists of 2 N-servers.
N-server is used in consideration that several packets can be transmitted through it with the same delay. So for example if we have link capacity of 2Mbps than two 1024 Kbyte packets can be transmitted with the same delay. (2 x 1024 x 1024)/(1024 x 1024) = 2
I assume that 2Mbps is the capacity in one direction, and it the same for another direction and transmission in both directions is independent. Like for example in Ethernet cable where some of links are used as input and some as output.

Here is configuration for 2Mbps/1ms delay Red Link: Number of servers is 2 and service time is 0.001. For 5Mbps/7ms delay Blue Link: Number of servers is 5 and service time is 0.007. For 3Mbps/3ms delay Green Link: Number of servers is 3 and service time is 0.003.
## Router 1
Each router in my system is different from each other. Router 1 is connected to hosts 1-3 and to routers 2 and 5. So R1 block has 10 connections, 5 of the are input and 5 are output connections.

Inside router 1 consists of 1 path combiner, 2 output switch, 1 attribute function and Single Server. From the start I would like to say that Single server is not actually needed. And it's serving time is set to 0. But In documentation of MATLAB it's said that it's good to put server after attribute function.
The main part of router is logic inside the attribute function.

We are looking at dest attribute of a packet. If the packets destination is to host 1, 2 or 3 than we send packet to respective host output connection on first Output Switch, which is configured according to port attribute of the packet. Otherwise if the packet's destination is something else we send our packet to second Output Switch, which is configured to send to the first non-blocking port. And first connection of it is connected to Blue Link. Blue link has higher capacity so it's higher priority.

## Router 2
Router 2 is the most simple router, because it has just two link connections. Single Server has 0 serving time. Set attribute block sets rfrom attribute to incoming packets. rfrom = 1 if packet comes from Router 1, or rfrom = 3 if packet comes from Router 3. Attribute Function block containts:
Depending on this attribute we determine where the packet will go next. If packet came from Router 1 then it will go to Router 3, or if packet came from Router 3 it will go to Router 1, that is it.
## Router 3

Router 3 is a little bit trickier. Here the same as in router 2 we have Set Attribute block on inputs which set rfrom attribute (2,5,4 respectively) to incoming packets. We have 3 link connections, two of them are blue with higher priority and on green link. The logic of this structure is like this. If incoming packet comes from router 2, then send it to router 4, or wise versa. If incoming packet comes from router 5 and it's destination is hosts between 1-3, then send packet to router 2 otherwise to router 4. In other cases send packet to router 5. Here is attribute function:
First Output Switch is configured to switch on port attribute of the packet. The second level Output Switches are configured to switch on first non-blocking port.
## Router 4

Router 4 looks pretty much the same as Router 3 but the Attribute function is a little bit different.
The logic of this structure is like this. If incoming packet comes from router 3, then send it to router 7, or wise versa. If incoming packet comes from router 6 and it's destination is host between 1-3, then send packet to router 3 otherwise to router 7. In other cases send packet to router 6.
## Router 5
Router 5 is the same as routers 3 and 4. If incoming packet comes from router 1, then send it to router 6, or wise versa. If incoming packet comes from router 3 and it's destination is host between 1-3, then send packet to router 1 otherwise to router 6. In other cases send packet to router 3.

## Router 6
Router 6 is the same as routers 3,4 and 5.

If incoming packet comes from router 5, then send it to router 7, or wise versa. If incoming packet comes from router 4 and it's destination is host between 1-3, then send packet to router 5 otherwise to router 7. In other cases send packet to router 4.
## Router 7
Router 7 is like router 1.

If incoming is from routers subnetwork then send to respective host, otherwise send to the first non blocking router. And Router 4 is prioritized because of link capacity.